Summary of Findings:

Parking and Trip Generation Study

For Assisted Living Facilities

District 5 – Tennessee Section: Memphis, TN

Submitted to:

Ed Stollof, AICP

Institute of Transportation Engineers 
Senior Director, Safety Programs 
1099 14th Street NW, Suite 300 West 
Washington, DC  20005 
Phone: (202) 289-0222 x 132
estollof@ite.org

Submitted by:

University of Memphis ITE Student Chapter

University of Memphis

Department of Civil Engineering

104 Engineering Sciences Bldg.

Memphis, TN 38152 – 3180

Phone: 901.678.3287

Fax: 901.678.3026

ITE Student Chapter Contact:

Ethan Skaggs – ITE Student Chapter President

ewskaggs@memphis.edu

Submitted:

May 6, 2008

Introduction

The objective of this study is to collect relevant trip generation and parking data for the International Board of ITE, in order to supplement the existing data in the ITE trip Generation Manual. Students from The Universiy of Memphis ITE Student Chapter as well as the CIVL 3161 – Transportation Systems Engineering course collected data to determine trip generation and parking demand for assisted living facilities, land use code 254. Three separate facilities in the Memphis area were selected for this trip generation and parking study.

Description of Study Sites

The three assisted living sites selected for this study were: Belmont Village, Southerland Place, and The Point at Kirby Gate. These sites are located throughout the Memphis metropolitan area. Facility information for the selected sites is given in Table 1.

Table 1. Facility Information

|  | Belmont Village | The Point at Kirby Gate | Southerland Place |
| --- | --- | --- | --- |
| Address | 6605 Quail Hollow Rd., Memphis TN, 38120 | 6480 Quince Road, Memphis TN, 38119 | 7701 Poplar Ave., Germantown TN, 38138 |
| Site Size (sq. ft.) | 85,347 | 37,822 | 31,420 |
| Dwelling Units | 120 | 53 | 50 |
| Dwelling Units Occupancy | 98% | 85% | 100% |
| Parking Spaces Available | 93 (5 handicap) | 36 (2 handicap) | 35 (2 handicap) |
| Employees | 72 | 30 | 27 |
| Facility Shuttle | Yes car (individual trips) van (20 person for group activities) | Yes van (14 person for individual trips and group activities) | Yes van (14 person for individual trips and group activities) |
| Date of Surveys: Weekday Sunday | 03/26/2008 03/30/08 | 04/01/08 04/06/08 | 03/27/2008 04/06/08 |

Methodology

Selection of the three study sites was determined based on first securing an owner/operator who was willing to allow members of our team to conduct the study at their facility. After the study facilities were established, a schedule to collect the necessary data was developed, to equally distribute man hours amongst participating students. Both weekday peak hour and generator peak hour trip generation data were collected for all facilities.  Based on interviews conducted with managers at each site, Sundays midday were identified as peak visiting times for all facilities, and a Sunday trip generation count was collected for each during the hours of 11:00 am – 3:00 pm.

Peak weekday parking demand was collected every hour from 7 AM – 6 PM, at each facility. Sunday parking counts were collected every hour from 11:00 am – 3:00 pm.

Two person teams were sent to each site and assigned to observe and record the number and type of vehicle entering and exiting the property along with the number of passengers in each vehicle.  The raw data collected from the generators is recorded in the attached ITE data sheets. A summary of the trip generation and parking demand data is presented in the following tables.

Table 2. Trip Generation – Vehicle Trips

|  |  | Dwelling Units | Vehicles | Vehicle Trips per Dwelling Unit |
| --- | --- | --- | --- | --- |
| AM Peak Hour (7-9AM) |  |
| 8:00-9:00 AM | Belmont Village | 120 | 24 | 0.20 |
| 8:00-9:00 AM | The Point at Kirby Gate | 53 | 10 | 0.19 |
| 7:45-8:45 AM | Southerland Place | 50 | 10 | 0.20 |
| PM-Peak Hour (4-6PM) |  |  |  |
| 4:15-5:15 PM | Belmont Village | 120 | 35 | 0.29 |
| 5:00-6:00 PM | The Point at Kirby Gate | 53 | 15 | 0.28 |
| 4:00-5:00 PM | Southerland Place | 50 | 15 | 0.30 |
| Weekend Generator Peak Hour (11AM-3PM) |  |  |  |
| 1:30-2:30 PM | Belmont Village | 120 | 34 | 0.28 |
| 12:00-1:00 PM | The Point at Kirby Gate | 53 | 16 | 0.30 |
| 12:45-1:45 PM | Southerland Place | 50 | 16 | 0.32 |

Table 3. Parking Demand

|  | On-Site Parking Demand | Total Vehicles per Dwelling Unit |
| --- | --- | --- |
|  | Belmont Village | The Point at Kirby Gate | Southerland Place | Belmont Village | The Point at Kirby Gate | Southerland Place |
| 7:00-7:59AM | 23 | 6 | 9 | 0.19 | 0.11 | 0.18 |
| 8:00-8:59AM | 25 | 8 | 9 | 0.21 | 0.15 | 0.18 |
| 9:00-9:59AM | 41 | 13 | 11 | 0.34 | 0.25 | 0.22 |
| 10:00-10:59AM | 31 | 17 | 18 | 0.26 | 0.32 | 0.36 |
| 11:00-11:59AM | 52 | 17 | 20 | 0.43 | 0.32 | 0.40 |
| 12:00-12:59PM | 52 | 13 | 22 | 0.43 | 0.25 | 0.44 |
| 1:00-1:59PM | 58 | 13 | 24 | 0.48 | 0.25 | 0.48 |
| 2:00-2:59PM | 48 | 13 | 23 | 0.40 | 0.25 | 0.46 |
| 3:00-3:59PM | 53 | 12 | 23 | 0.44 | 0.23 | 0.46 |
| 4:00-4:59PM | 48 | 13 | 22 | 0.40 | 0.25 | 0.44 |
| 5:00-5:59PM | 41 | 11 | 21 | 0.34 | 0.21 | 0.42 |
| 6:00-6:59PM | 34 | 10 | 22 | 0.28 | 0.19 | 0.44 |
|  |  |  | Peak Parking | 0.48 | 0.32 | 0.48 |

Conclusion

Assisted living communities consist of mostly non-driver oriented residents, consequently lowering the frequency of trips generated at such facilities.  Most assisted living facilities provide transportation, i.e. facility buses or vans, to residents, also reducing the number of trips generated by such sites.  Care was taken to avoid data collection during holidays or extreme weather conditions, and to select sites that had high levels of occupancy.  Thus, the findings from this study should be representative of many similar assisted living facilities.